## Slide 1
Scallop migration is a parity break that down-gradient closures cannot reproduce
The story in one line
Scallops on the bed drift downstream AND we'd like our model to capture it, BUT a symmetric down-gradient model literally cannot point downstream, THEREFORE migration is a clean, measurable test the standard closure fails.
Presenter: [your name] · [affiliation] · [ORCID]
code & data: github.com/oss2444/K
Notes: Hook with a paradox: a model can fit the shape of a bedform perfectly and still get the physics wrong — because it can't say which way the form moves. That 'which way' is the whole game.

## Slide 2
Think of a clock with no difference between tick and tock
A down-gradient closure is mirror-symmetric: it has no built-in sense of 'downstream'.
It's like a clock whose tick and tock are identical — it can't tell you which way time runs.
But scallops DO run one way. So the closure is missing something structural, not just tuned wrong.
A symmetric closure forces the migration speed to be exactly zero — by construction.
Paper 3 · Scallop parity break · github.com/oss2444/K
2
Notes: Symmetry sounds harmless, even elegant. The point of this talk is that this particular symmetry is a defect: it forces a real, observed direction to be exactly zero. Let the clock image sit before the formal statement.

## Slide 3
Migration is the out-of-phase part of the bed's response — the imaginary part
Harmonic decomposition of the wall flux: Re(s) vs Im(s).
in-phase (Re)
grows / decays the scallop
out-of-phase (Im)
MOVES the scallop — migration
phase ψ
the single clean observable
Paper 3 · Scallop parity break · github.com/oss2444/K
3
Notes: Here's the mechanism in one line. Drive the bed with a topographic wave and read the flux response. The in-phase part grows or decays the bedform; the out-of-phase (quadrature) part moves it. Migration speed is literally the imaginary part of a complex response.

## Slide 4
A symmetric closure has zero imaginary part — so it cannot migrate, ever
K-theory: Im(s) = 0
no migration possible
structural
not a tuning gap
prediction
migration speed = 0 exactly
Paper 3 · Scallop parity break · github.com/oss2444/K
4
Notes: This is the keystone. Because down-gradient closures are parity-symmetric, their response has no imaginary part: Im(s) = 0. That's not a small error you can tune away — it's a structural impossibility. The closure predicts a migration speed of exactly zero.

## Slide 5
In the resolved solver, the scallop genuinely migrates — the parity break is measured
Im(s) ≠ 0
measured in the solver
I = |tan ψ|/2π
the migration index
closure = 0
contradicted by the solver
Scallop geometry used in the harmonic probe.
VERIFIED — migration measured in the resolved solver
Paper 3 · Scallop parity break · github.com/oss2444/K
5
Notes: And here's the evidence: the full solver produces a non-zero imaginary part and real downstream migration on the same bed where the closure gives zero. We package it as an index I = |tan ψ|/2π. The model and the closure disagree, and the solver is right.

## Slide 6
The phase test is constant-free and needs no temperature difference
constant-free
no absolute calibration
ΔT-free
no temperature difference needed
field-testable
from geometry + flow alone
FALSIFIED — the K² curvature and Mullins–Sekerka |k| ansätze (wavelength test)
Paper 3 · Scallop parity break · github.com/oss2444/K
6
Notes: Why this is a good test: the phase observable needs no absolute calibration and no ΔT. You can read the parity break from bedform geometry and the flow alone — so it's checkable in the field, not just in a solver. Note in passing: the K² curvature and Mullins-Sekerka |k| ansätze are falsified.

## Slide 7
What is verified, what is falsified, what is still open
VERIFIED
• Migration = Im(s) parity break (solver)
• Closure forced to Im(s)=0
• Robust across amplitude & drive
• Constant-free index I=|tan ψ|/2π
FALSIFIED
• K² curvature ansatz
• Mullins–Sekerka |k| ansatz
OPEN
• One open gate (bounded)
• Field measurement on a real reach
Paper 3 · Scallop parity break · github.com/oss2444/K
7
Notes: Be plain: the falsified ansätze are competitors we ruled out; the open item is a single bounded gate.

## Slide 8
The takeaway: migration is a clean, measurable failure of down-gradient closures
one clean test
bedform migration / phase ψ
closure must say 0
reality says otherwise
reproducible
github.com/oss2444/K
Paper 3 · Scallop parity break · github.com/oss2444/K
8
Notes: Land it: if you want one experiment to tell whether a down-gradient closure is missing the reactive physics, measure bedform migration — it must be zero in the closure and isn't in reality. Connects to Paper 1's reactive part and NR2/NR4/NR9.